## Slide 1: Wine Blending

## Slide 2: Blending Goals
A better wine (balance, complexity)
Consistent year after year
Lower cost
Mask Faults (beware of disaster, making a sound partner bad)
Getting a wine to “peak” at the time it is consumed

## Slide 3: BALANCE
DRY RED WINES
  ACIDITY
  SWEETNESS
  ALCOHOL %
  TANNIN (most difficult to manage, develops and transforms)
      Can mask the fruity character of a blend
  Acidity and alcohol can offset higher concentration of the other
  Alcohol and tannin reinforce each other

## Slide 4
Acidity | Tannin | Alcohol | 
 | BALANCED |  | 
LOW | HIGH | LOW/MED/HIGH | 
HIGH | LOW | MED/HIGH | 
MED | MED | LOW/MED/HIGH | 

## Slide 5
ACIDITY | TANIN | ALCOHOL | 
 | UNBALANCED |  | 
LOW | LOW | HIGH | 
HIGH | HIGH | LOW | 

## Slide 6: Balance
Acidity
Residual Sugar
Alcohol content
Tannin
Oak or oak varieties
M/L character & fruit
Color

## Slide 7: What to Blend
Same varietals from different vineyards
Same varietals , different vintages
Different, “compatible” varietals

## Slide 8: Experiment
Document
Watch your numbers
Use a spreadsheet

## Slide 9
Blend Calculations
component | gal. | % blend | ph | TA | SO2 | RS | Alc
Norton | 25 | 56 | 3.4 | 1.0 | 55 | 0.1 | 12.5
Chamb | 15 | 33 | 3.5 | 0.7 | 55 | 0.1 | 12.5
Cabernet | 5 | 11 | 3.75 | 0.5 | 60 | 0.3 | 14.5
Totals | 45 |  | 3.47 | 0.844 | 55.6 | 0.12 | 12.7

## Slide 10: Testing
Multiple tasters
Taste a variety of blends (3:1,1:1, 1:3) along with unblended components
Practice improves success
Blending Math & Pearsons Square
    % alcohol/vol of a blend = (AxD) + (BxE)/(D+E)
      A = % alcohol /vol of 1st wine
      B = % alcohol / vol of 2nd wine
      D = Volume 1st wine
      E = Volume of 2nd wine
Blending 3,4 or more wines with multiple goals
Store a desire blend for a month or two and reevaluated

## Slide 11
A
B
D
E
C
A = concentration of the wine to be used
B = concentration of the wine to be corrected
C = calculated or desired concentration
D = # of parts of the wine to be used is = to C-B
E = # of parts of the wine to be corrected and is = to A-C
13.5
12.5
12
1.0
.5

## Slide 12
The Blending Process
Blending requires a plan
Establish a style, goals
Quantitatively asses the element concentration in the blended trials